## Slide 1
ROADLYY
Urban Traffic Intelligence & Multi-Horizon Spatial-Temporal ML Engine
Domain: AI in Smart Cities & Urban Mobility
Team: Culers
End-to-End Predictive Traffic Analytics, Graph Shockwaves & Detour Optimization

## Slide 2
1. The Urban Gridlock Problem
Non-Linear Congestion & Cascading Shockwave Bottlenecks
Reactive, Not Predictive
Current navigation systems and traffic centers only detect congestion after it has already formed, causing massive driver delays.
Upstream Spillover Shockwaves
A single lane blockage or crash does not stay isolated. Queues spill backward, creating compounding gridlock across feeder links.
Lack of ROI-Driven Planning
Municipalities lack data-driven decision frameworks to quantify which infrastructure upgrades yield the highest delay reductions.

## Slide 3
2. Roadlyy Solution Architecture
High-Throughput End-to-End Intelligence Pipeline
1. Graph Ingestion Core
Directed urban road graph (NetworkX) modeling 436 links and 120 nodes with physical lane capacities and speed limits.
2. Multi-Horizon ML Models
HistGradientBoosting regressors trained on 1.88M+ rows predicting Speed, Flow, and Congestion across +15m, +30m, +45m, and +60m.
3. Interactive Command Center
Sub-millisecond FastAPI REST API powering a dark-monochrome Leaflet geospatial operations dashboard.

## Slide 4
3. Metropolitan Graph & Dataset Scale
High-Fidelity Spatial-Temporal Telemetry Across 19 Continuous Days
1.88M+ Observations
Trained and validated on 1,884,960 records with 5-minute granular velocity, flow volume (vph), and density indices.
436 Road Links & 120 Nodes
Models Hyderabad metropolitan core across Motorways (60 km/h), Arterials (50 km/h), Collectors (40 km/h), and Local streets.
BPR Physics & Weather Friction
Integrates Bureau of Public Roads (BPR) speed-flow-density curves with real-time temperature and rainfall intensity (mm/h).

## Slide 5
4. Multi-Horizon AI Forecasting Engine
Validated Accuracy Across 481,344 Targets (HistGradientBoosting)
+15 min
91.0% R²
MAE: 2.38 km/h
Tactical immediate forecasting
+30 min
89.2% R²
MAE: 2.85 km/h
Short-term trend projection
+45 min
87.4% R²
MAE: 3.12 km/h
Medium-range buildup alert
+60 min
85.8% R²
MAE: 3.45 km/h
1-Hour strategic horizon

## Slide 6
5. Shockwave Propagation & Dynamic Detours
Graph-Aware Spillover Mitigation & Automated Rerouting
Topological Feeder Analysis
When a corridor is disrupted, the graph engine traces upstream in-edges to compute spillback speed drops and queue accumulation.
Dynamic Detour Routing
Computes the optimal alternative shortest sub-graph path bypassing the incident link with exact detour length and added travel time penalty.
Incident Pulse Beacons
High-contrast visual hierarchy: White incident beacon (!), silver upstream feeder alerts, and dashed white detour route lines.

## Slide 7
6. What-If Sandbox & Capital Planning
Interactive Scenario Evaluator & 90-Candidate ROI Matrix
Live Test Case Evaluator
Injects custom lane blockages, accidents, or storms on any link. Normalizes inputs (4 -> R0004) with dynamic physics synthesis.
90 Planning Candidates
Evaluates Lane Additions, Capacity Upgrades, Turn Lanes, Signal Retiming, and Connectors for city authorities.
Quantitative ROI Score
Ranked by Weekly Vehicle Delay Hours Saved per Unit Cost Index (ROI = Delay Hours / Cost Index).

## Slide 8
ROADLYY — Smart City Impact
Predictive. Graph-Aware. Production-Ready.
Domain: AI in Smart Cities | Team: Culers
GitHub Repository: https://github.com/manuroszonero/roadlly
Transforming Metropolitan Traffic Management from Firefighting to Foresight